## Slide 1
Jerry Breecher
OPERATING SYSTEMS
History and Hardware

## Slide 2
This is the simplest animal with a “brain”
Caenorphabditis elegans
C. elegans is one of the simplest organisms with a nervous system. This system comprises 302 neurons the pattern of which has been comprehensively mapped, in what is known as a connectome.
There are sensory neurons, motor neurons, and interconnecting neurons.
There are
16 chemical sensor neurons,
2 thermal sensors,
28 mechanical (touch) neurons,
4 light sensors,
and additional neurons and synapsis for learning and memory.

## Slide 3
Dots represent the cell bodies of neurons; long lines represent the neurons' axons and dendrites.
Scientists were able to label every one of the 302 neurons as either a sensory neuron (one that collects information from the environment, such as temperature or pressure); a motor neuron that controls muscles; or an interneuron, which connects the two.
Caenorphabditis elegans

## Slide 4
Inside an I-Phone
There are Sensors Everywhere!
Sensor
Sensor
Sensor
Sensor
Sensor
Sensor

## Slide 5
What is an Operating System?
It’s the mechanism that connects the hardware’s inputs and outputs and provides an interface for a user.
The inputs and outputs are what determines the OS. As the hardware and user changes, so does the OS.
So let’s spend a few minutes looking at the history of computer hardware – from that we can see why the OS is what it is.

## Slide 6
Really??
1943
  T.J. Watson (created IBM): “ I think there is a world market for maybe five
  computers.”
Fast forward … 1950
  There are maybe 20 computers in the world
    They were unbelievably expensive
    Imagine this: machine time is more valuable than person time!
    So: efficient use of the hardware is paramount
  Operating systems are born to use this valuable resource

## Slide 7
What is an Operating System?
In the very beginning…
  OS was just a library of code that you linked into your program; programs were loaded in their entirety into memory, and executed. Your program and the OS were one!
    “OS” had an “API” that let you control the disk, control the printer, etc.
  Interfaces were literally switches and blinking lights
  When you were done running your program, you’d leave and turn the computer over to the next person
CPU
Diskosaurus
Memory
Printer
Input Device

## Slide 8
What is an Operating System?
Disk Controller
The diskosaurus was really slow
Add hardware so that the disk could operate without tying up the CPU
  Disk controller
Hotshot programmers could now write code that:
  Starts an I/O
  Goes off and does some computing
  Checks if the I/O is done at some later time
Upside
  Helps increase (expensive) CPU utilization
Resident Monitor
Everyone was using the same library of code
Why not keep it in memory?
While we’re at it, make it capable of loading Program 4 while running Program 3 and printing the output of Program 2
  SPOOLing – Simultaneous Peripheral Operations On-Line
What new requirements does this impose?

## Slide 9
What is an Operating System?
The IBM 1620 – the machine on which I did my Ph.D. research.
The processor of the 1620 was listed at $64K, with another $40Kfor 20,000 digits of core storage and $10K for the for paper tape. Total cost of $114K or about $1M in today’s dollars.
Programming required loading pass 1 of the Fortran II compiler, then the source code, producing an intermediate tape, loading the 2nd pass of the compiler along with the intermediate tape.
Adding two 10-digit numbers together on the 1620 took 960µs, including loading the operands and storing the results. That’s about 0.001 MIPS.
Paper tape punch/reader.

## Slide 10
What is an Operating System?
IBM System 360
To further increase system utilization, multiprogramming OSs were invented
keeps multiple runnable jobs loaded in memory at once
overlaps I/O of one job with computing of another
  while one job waits for I/O completion, another job uses the CPU
Can get rid of asynchronous I/O within individual jobs
  Life of application programmer becomes simpler; only the OS programmer needs to deal with asynchronous events.
How do we tell when devices are done?
  Interrupts
  Polling
  What new requirements does this impose?

## Slide 11
What is an Operating System?
1980 Data General MV8000 – first machine I worked on in my Software Engineering career.
1 MIPS processor, 1 Mbyte of memory, 32-bit address space.
Board is discreet logic – no microprocessors.
Disk is 200 Mbytes – size of a washing machine.

## Slide 12
Operating System Genealogy

## Slide 13
Operating System – Power Usage
The job of the OS is to make the most of the hardware presented to it!
OS must figure out a way to reduce power usage.

## Slide 14
Operating System – Disk Characteristics
The job of the OS is to make the most of the hardware presented to it!
What is the relative performance win of putting more data on disk?

## Slide 15
Operating System – Disk Characteristics
The job of the OS is to make the most of the hardware presented to it!

## Slide 16
Operating System – Disk Characteristics
The job of the OS is to make the most of the hardware presented to it!
Disks are “big” and “cheap”, but they aren’t “close”.

## Slide 17
Operating System - Memory
The job of the OS is to make the most of the hardware presented to it!
Memory is cheap and fast – caches allow data to be kept close to the processor.

## Slide 18
Operating System – Relative Performance
The job of the OS is to make the most of the hardware presented to it!
How all these speeds and sizes play together.

## Slide 19
Operating System – the future?
A map of the 4 billion nodes in the Internet. How does the OS enable it to operate?
The intelligence is in the nodes, not in the connecting wires and network.

## Slide 20: ManyCore Chips: The future is here
Operating System – the future?
Intel 80-core Enterprise chip (Feb 2007)
  80 simple cores
  Two FP-engines / core
  Mesh-like network
  100 million transistors
  65nm feature size
Intel Single-Chip Cloud Computer (August 2010)
  24 “tiles” with two cores/tile
  24-router mesh network
  4 DDR3 memory controllers
  Hardware support for message-passing
Intel 10-core desktop chip (2016)

## Slide 21
Operating System – the future?
Cache:
  L1: 32K Inst, 32K Data (3 clock access)
  L2: 256K (8 clock access)
  Shared L3: 3MB – 20MB (not out yet)
Package: LGA 1155
  1155 pins
  95W design envelope
Transistor count:
  504 Million (2 cores, 3MB L3)
  2.27 Billion (8 cores, 20MB L3)

## Slide 22: All this leads to Increasing Software Complexity
Operating System – the future?
http://www.informationisbeautiful.net/visualizations/million-lines-of-code/
Puts all this in perspective

## Slide 23
Hardware Support For Fundamental OS Operations
Thread
  Single unique execution context
  Program Counter, Registers, Execution Flags, Stack  Hardware support
Address Space with Translation
  Programs execute in an address space that is distinct from the memory space of the physical machine  Hardware support
Processes
  An instance of an executing program is a process consisting of an address space and one or more threads of control  Hardware support
Dual Mode (OS and user)/Protection
  Only the “system” has the ability to access certain resources  Hardware support
  The OS and the hardware are protected from user programs and user programs are isolated from one another by controlling the translation from program virtual addresses to machine physical addresses

## Slide 24
Hardware Support For Fundamental OS Operations
Certain special registers hold the context of thread
  Stack pointer holds the address of the top of stack
    Other conventions: Frame Pointer, Heap Pointer, Data
  May be defined by the instruction set architecture or by compiler conventions
Thread: Single unique execution context
  Program Counter, Registers, Execution Flags, Stack
A thread is executing on a processor when it is resident in the processor registers.
PC register holds the address of executing instruction in the thread.
Registers hold the root state of the thread.
  The rest is “in memory”
Special Word!
Thread

## Slide 25
Hardware Support For Fundamental OS Operations
0x000…
0xFFF…
code
Static Data
heap
stack
Address space  the set of accessible addresses + state associated with them:
  For a 32-bit processor there are 232 = 4 billion addresses
What happens when you read or write to an address?
  Perhaps Nothing
  Perhaps acts like regular memory
  Perhaps ignores writes
  Perhaps causes I/O operation
    (Memory-mapped I/O)
  Perhaps causes exception (fault)
These all depend on hardware support!
Address Space with Translation

## Slide 26
Hardware Support For Fundamental OS Operations
Address Space with Translation
Processor
registers
PC:
0x000…
0xFFF…
Code Segment
Static Data
heap
stack
instruction
SP:
What’s in the code Segment?
What’s in the Static Data Segment?
What’s in the Stack Segment?
  How is it allocated? How big is it?
What’s in the Heap Segment?
  How is it allocated? How big?

## Slide 27
Hardware Support For Fundamental OS Operations
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
Processes – especially multiple processes

## Slide 28: How can we give the illusion of multiple processors?
Hardware Support For Fundamental OS Operations
Processes – especially multiple processes
vCPU3
vCPU2
vCPU1
Shared Memory
Assume a single processor. How do we provide the illusion of multiple processors?
  Multiplex in time!
Each virtual “CPU” needs a structure to hold:
  Program Counter (PC), Stack Pointer (SP)
  Registers (Integer, Floating point, others…?)
How switch from one virtual CPU to the next?
  Save PC, SP, and registers in current state block
  Load PC, SP, and registers from new state block
What triggers switch?
  Timer, voluntary yield, I/O, other things
vCPU1
vCPU2
vCPU3
vCPU1
vCPU2
Time

## Slide 29: Concurrency
Hardware Support For Fundamental OS Operations
Processes – especially multiple processes
The basic problem of concurrency involves resources:
  Hardware: single CPU, single DRAM, single I/O devices
  Multiprogramming API: processes think they have exclusive access to shared resources
OS has to coordinate all activity
  Multiple processes, I/O interrupts, …
  How can it keep all these things straight?
Basic Idea: Use Virtual Machine abstraction
  Simple machine abstraction for processes
  Multiplex these abstract machines

## Slide 30: Concurrency
Hardware Support For Fundamental OS Operations
Processes – especially multiple processes
All virtual CPUs share same non-CPU resources
  I/O devices the same
  Memory the same
Consequence of sharing:
  Each thread can access the data of every other thread (good for sharing, bad for protection)
  Threads can share instructions (good for sharing, bad for protection)
  Can threads overwrite OS functions?
This (unprotected) model is common in:
  Embedded applications
  Windows 3.1/Early Macintosh (switch only with yield)
  Windows 95—ME (switch with both yield and timer)

## Slide 31
Hardware Support For Fundamental OS Operations
Protection
Operating System must protect itself from user programs
  Reliability: compromising the operating system generally causes it to crash
  Security: limit the scope of what processes can do
  Privacy: limit each process to the data it is permitted to access
  Fairness: each should be limited to its appropriate share of system resources (CPU time, memory, I/O, etc)
It must protect User programs from one another
  Primary Mechanism: limit the translation from program address space to physical memory space
  Can only touch what is mapped into process address space
Additional Mechanisms:
  Privileged instructions, in/out instructions, special registers
  syscall processing, subsystem implementation
    (e.g., file access rights, etc)

## Slide 32
Hardware Support For Fundamental OS Operations
Protection
Process: execution environment with Restricted Rights
  Address Space with One or More Threads
  Owns memory (address space)
  Owns file descriptors, file system context, …
  Encapsulate one or more threads sharing process resources
Why processes?
  Protected from each other!
  OS Protected from them
  Processes provides memory protection
  Threads more efficient than processes (later)
  Fundamental tradeoff between protection and efficiency
    Communication easier within a process
    Communication harder between processes
Application instance consists of one or more processes

## Slide 33: Single and Multithreaded Processes
Hardware Support For Fundamental OS Operations
Protection
Threads encapsulate concurrency: “Active” component
Address spaces encapsulate protection: “Passive” part
  Keeps buggy program from trashing the system
Why have multiple threads per address space?

## Slide 34
Hardware Support For Fundamental OS Operations
Protection
Hardware provides at least two modes:
  “Kernel” mode (or “supervisor” or “protected”)
  “User” mode: Normal programs executed
What is needed in the hardware to support “dual mode” operation?
  a bit of state (user/system mode bit)
  Certain operations / actions only permitted in system/kernel mode
    In user mode they fail or trap
  UserKernel transition sets system mode AND saves the user PC
    Operating system code carefully puts aside user state then performs the necessary operations
  KernelUser transition clears system mode AND restores appropriate user PC
    return-from-interrupt

## Slide 35
Hardware Support For Fundamental OS Operations
Protection
Syscall
  Process requests a system service, e.g., exit
  Like a function call, but “outside” the process
  Does not have the address of the system function to call
  Like a Remote Procedure Call (RPC) – for later
  Marshall the syscall id and args in registers and exec syscall
Interrupt
  External asynchronous event triggers context switch
  eg. Timer, I/O device
  Independent of user process
Trap or Exception
  Internal synchronous event in process triggers context switch
  e.g., Protection violation (segmentation fault), Divide by zero, …
All 3 are an UNPROGRAMMED CONTROL TRANSFER
  Where does it go?
How can a user program safely get to the OS?

## Slide 36
Hardware Support For Fundamental OS Operations
Protection
How can a user program safely get to the OS?
The goal is protecting the Operating System and others from malicious or ignorant users.
The User/Supervisor Mode and privileged instructions.
Concurrent threads might interfere with others. This leads to protection of resources by user/supervisor mode. These resources include:
  I/O Define I/O instructions as privileged; they can be executed only in Supervisor mode. System calls get us from user to supervisor mode.

## Slide 37
Hardware Support For Fundamental OS Operations
How Interrupts Work
Interrupt transfers control to the interrupt service routine generally, through the interrupt vector, which contains the addresses of all the service routines.
Interrupt architecture must save the address of the interrupted instruction.
Incoming interrupts are disabled while another interrupt is being processed to prevent a lost interrupt.
A trap is a software-generated interrupt caused either by an error or a user request.
An operating system is interrupt driven.

## Slide 38
Hardware Support For Fundamental OS Operations
These are the devices that make up a typical system.
Any of these devices can cause an electrical interrupt that grabs the attention of the CPU.
IO Support

## Slide 39
Hardware Support For Fundamental OS Operations
These are the devices that make up a typical system.
Any of these devices can cause an electrical interrupt that grabs the attention of the CPU.
IO Support

## Slide 40
Hardware Support For Fundamental OS Operations
IO Support
Sequence of events for processing an IO request.
Comparing Synchronous and Asynchronous IO Operations